# Interconnecting Computers: 
Architecture, Technology, and Economics

Butler Lampson

Modern computer systems have a recursive structure of processing and storage elements that are interconnected to make larger elements.  Above the lowest level of transistors and gates, the essential character of these connections changes surprisingly little over about nine orders of magnitude in time and space.  Here are some examples:

Functional units connected to registers and on-chip cache.

Processor chips connected to cache memories.

Multiple processors and caches connected to main memories.

Computing nodes connected by a message-passing LAN.

LANs bridged to form an extended LAN.

Networks connected in a wide-area internet.

All the computers in the world exchanging electronic mail.

The important properties of connections are latency, bandwidth, connectivity, availability, and cost.  The basic mechanism for connecting lots of things is multiplexing, but there are many ways to implement it.  This lecture describes some of these ways and considers how different levels of the recursive hierarchy interact.

# Interconnecting Computers:
Architecture, Technology, and Economics

Computer systems are made up of interconnected subsystems.

The structure and methods are similar across the board.

Structure = architecture

Methods = technology

Better silicon and fiber optics make all the subsystems more alike.

|  | Messages | Storage |
| --- | --- | --- |
| Two-party |  | or Storage is one party, or not. |
| Broadcast |  |  |
| Multi-party | Left and right nodes can be the same. |  |

# Examples of Messages

| System | Address | Sample address | Delivery |  |
| --- | --- | --- | --- | --- |
|  |  |  | Ordered | Reliable |
| J-machine | source route | 4 north, 2 east | yes | yes |
| 802 LAN | 6 byte flat | FF F3 6E 23 A1 92 | no | no |
| IP | 4 byte path | 16.12.3.134 | no | no |
| TCP | IP + port | 16.12.3.134 / 3451 | yes | yes |
| RPC | TCP + procedure | ... / OpenFile | yes | yes |
| E-mail | host name + user | lampson@src.dec.com | no | yes |

## Request-response is the most popular way to use messages

It adds no concurrency (unless there are failures)

# Examples of Storage

| System | Address | Sample address | Data value |  |
| --- | --- | --- | --- | --- |
| Main memory | 32-bit flat | 04E72A39 | 1, 2, 4, or 8 bytes |
| File system | path name | /udir/bwl/Mail/inbox/214 | 0-4 Gbytes |
| World Wide Web | protocol + host name + path name | http:// src.dec.com/ SRC/docs.html | typed, variable size |

# Universality

In the Turing tarpit everything is possible, but nothing is easy.

Alan Perlis

## Can simulate messages with storage, and vice versa

## Messages  storage

Send load and store messages to a ‘storage server’

## Storage  messages

Build message queues and poll them

Reinterpret load and store operations

# Performance

## Bandwidth

## Latency

## Connectivity

## Predictability

## Availability

# Implementation Components

An engineer can do for a dime what any fool can do for a dollar.

Anonymous

## Links

## Nodes

Converters

Multiplexers

Switches

## Effects of progress in silicon

2  every 1.5–2 years

Implies more concurrency, more complexity

## Fiber optics for long-haul communication

25 THz/fiber is available

# Physical Links

| Medium | Link | Bandwidth |  | Latency |  | Width |
| --- | --- | --- | --- | --- | --- | --- |
| Alpha chip | on-chip bus | 2.2 | GB/s | 3.6 | ns | 64 |
| PC board | RAMbus | 0.5 | GB/s | 150 | ns | 8 |
|  | PCI I/O bus | 133.0 | MB/s | 250 | ns | 32 |
| Wires | HIPPI | 100 | MB/s | 100 | ns | 32 |
|  | SCSI | 20 | MB/s | 500 | ns | 16 |
| LAN | FDDI | 12.5 | MB/s | 20 + | µs | 1 |
|  | Ethernet | 1.25 | MB/s | 100 + | µs | 1 |
| Wireless | WaveLAN | .25 | MB/s | 100 + | µs | 1 |
| Fiber | OC-48 | 300 | MB/s | 5 | µs/km | 1 |
| Coax cable | T3 | 6 | MB/s | 5 | µs/km | 1 |
| Copper pair | IDSN | 16 | KB/s | 5 | µs/km | 1 |
| Broadcast | CAP 16 | 3 | MB/s | 3 | µs/km | 6 MHz |

# Converter Nodes

## Internal converters are cheap

## Terminal converters are often messy

Interface to communication standard

Adapter hardware

Driver software

# Multiplexer Nodes

# Multiplexer Techniques

## Frequency division

## Code division

## Time division

Fixed

Variable — address in each packet or cell

## Multiplexer does arbitration

Scheduling, with flow control, and buffering

Usually centralized

Collision, backoff, and retry

Usually distributed

## Demultiplexer does addressing

Centralized, or distributed by broadcast

# Switch Nodes

(a) The usual representation of a switch

(b) A mux–demux implementation

# Parallel Switch Nodes

=

# Switch Examples

| Medium | Link | Bandwidth |  | Latency |  | Links |
| --- | --- | --- | --- | --- | --- | --- |
| Alpha chip | register file | 13.2 | GB/s | 3.6 | ns | 6 |
| Wires | Cray T3D | 85 | GB/s | 1 | µs | 2K |
|  | HIPPI | 1.6 | GB/s | 1 | µs | 16 |
| LAN | FDDI Gigaswitch | 275 | MB/s | 10–400 | µs | 22 |
|  | Switched Ethernet | 10 | MB/s | 100–1200 | µs | 8 |
| Copper pair | Central office | 80 | MB/s | 125 | µs | 50K |

# Recursion: Concatenating Links

Any idea in computing is made better by being made recursive.

Brian Randell

# Routing

## Turn an address into a path through the mesh

## Ways to do it					used in

Source routing	Multiprocessor grids
	Cascaded I/O busses

Virtual circuits	ATM

Hierarchical routing	Internet

Flat routing	802 LANs

# Deadlock

## Must have an ordering on link resources.

## On a grid, can use

East or west first, then north or south

# Recursion: Layers

There are three rules for writing a novel. 
Unfortunately, no one knows what they are.

Somerset Maugham

# Layers under TCP

| What | Why |  |
| --- | --- | --- |
| a TCP reliable transport link | function: | reliable stream |
| on an Internet packet link | function: | routing |
| on PPP header compression protocol | performance: | space |
| on HDLC data link protocol | function: | packet framing |
| on a 14.4 Kbit/sec modem line | function: | byte stream |
| on an analog voice telephone line | compatibility |  |
| on a 64 Kbit/sec line multiplexed | function: | bit stream |
| on a T1 line multiplexed | performance: | aggregation |
| on a T3 line multiplexed | performance: | aggregation |
| on an OC-48 fiber | performance: | aggregation |

# Layers under E-mail

| What | Why |  |
| --- | --- | --- |
| mail folders | function: | organization |
| on a mail inbox | function: | storage |
| on SMTP mail transport | function: | routing |
| on FTP file transport | function: | char arrays |
| on TCP reliable transport link | . . . |  |

# Layers under Memory

| What | Why |  |
| --- | --- | --- |
| load from cache | function: | data access |
| miss to second level cache or miss to other processors or reference on I/O bus | performance: function: function: | space sharing device access |
| miss to RAM or miss to network | performance: function: | space sharing |
| page fault to disk | performance: | space |

# Fault Tolerance

## Mirroring

Duplicate components

Detect errors

Ignore bad components

## Retry: no state change on error

Detect errors and retry

## Recovery

Checkpoint

Detect errors

Crash

Reconfigure without the bad components

Retry from the checkpoint

## Failover to backup component

## What about timeouts? Fault tolerance requires real time.

# Conclusions

## Uniform at many different scales

Storage and message interfaces

Links, converters, and switches

Compose by concatenation, routine, and layering

Bandwidth, latency, and connectivity

Congestion, flow control, and buffering

## Reasons

These are good ideas

2  advances in silicon encourage similar designs